Quansheng UV-K5/UV-K6 Scanning Facility

Last Update Oct. 26, 2023
by Ken Hansen, N2VIP

This note is to explain how the UV-K5/UV-K6 memory channel scan operates. The UV-K5/UV-K6 has a unique scan facility, in someways it is like the Memory Group function on some Yaesu radios, in otherways it is very unique.
These are the relevant menu settings in the radio:
25	S-ADD1	Participate in Scanlist 1 (off=0, on=1)	per channel
26	S-ADD2	Participate in Scanlist 2 (off=0, on=1)	per channel
31	S-LIST	Chanel Scan List Select (1, 2)	per channel
32	SLIST1	Channel Scan List 1 Configuration	global
33	SLIST2	Channel Scan List 2 Configuration	global
A reminder - in radios like Baofeng and Quansheng some menu settings are global in scope, meaning the setting affects all channels (like TOT, Time-out Timer) and some are per channel (like TXP, Output Power).
To enable memory channel scanning, you need to be in memory channel mode and then long press the "* Scan" key to begin scaning. As noted above, the radio has two Scanlists (1 and 2), and starting the Scan function will scan the scanlist in the S-LIST setting for the channel you are monitoring/set to. For example, if I have S-LIST set to the value 1, my radio will commence to scanning all programmed memory channels with S-ADD1 set to "1", or "on", meaning the channel is included in Scanlist 1. A channel can be part of either one of the Scanlists, both of the Scanlists, or neither Scanlist based on the values in S-ADD1 and S-ADD2 settings.
The SLIST1 and SLIST2 settings contains the channels in the respective Scanlist - you can not change the values in either setting, you can only review them by scrolling thru the channel numbers using the Up/Down arrow buttons on the radio panel. To add/remove channels from either Scanlist, you would adjust the settings S-ADD1 and S-ADD2 for the channels you want to add or remove from either Scanlist.
How would you use this? Lets work thru a simple example.
Imagine I have five channels programmed into my radio, two are local repeaters in my hometown (CH-001 and CH-002), two channels are repeaters near my workplace (CH-003 and CH-004), and the fifth channel is the national simplex channel (CH-005). Now, imagine I want a Scanlist for my home repeaters and another for the repeaters by my workplace, and I want the national simplex channel included in both Scanlists, like this:
Scanlist 1	(Home)	CH-001, CH-002, CH-005
Scanlist 2	(Work)	CH-003, CH-004, CH-005
So to configure my radio, I would adjust the following settings per channel, as shown:
CH-001 and CH-002 Settings
25	S-ADD1	"on"
26	S-ADD2	"off"
31	SLIST	"LIST1"
CH-003 and CH-004 Settings
25	S-ADD1	"off"
26	S-ADD2	"on"
31	SLIST	"LIST2"
CH-005 Settings
25	S-ADD1	"on"
26	S-ADD2	"on"
31	SLIST	"LIST1" (or "LIST2", it makes no difference for this example)
To scan my Home repeaters, i need to set my radio to either CH-001 or CH-002, then long-press the "* Scan" button, and my radio will scan the list of channels pointed to in the SLIST setting for the channel I am set to. In the above example, if I am on CH-001 or CH-002, I will scan the channels in SLIST1, if I am on either on CH-003 or CH-004 I'll scan the channels in SLIST2.
Channels must have an SLIST setting of either "LIST1" or "LIST2" in case the user activates the scan function while on that channel, but as noted previously every channel does not need to be included in either Scanlists.